## Slide 1
Computer Logic & Design
Lecture 03
Copyrights: Dr Waseem Ikram

## Slide 2: Recap
Number System Conversion
  Sum-of-Weights for converting to decimal
  Repeated division for converting from decimal
Binary Arithmetic
  Similar to Decimal Arithmetic
  Multiplying by a constant by shifting left
  Dividing by a constant by shifting right

## Slide 3: Recap
Representing Numbers
  Unsigned
  Signed Magnitude
  2’s Complement

## Slide 4: 2’s Complement form
1’s complement form
2’s complement form
Binary number 01101 (13)
1’s complement 10010
+ 1
2’s complement 10011 (-13)
Notes: Informing the digital system beforehand to deal with a number as signed or unsigned is inconvenient
Signed binary numbers are represented in their 2’s complement form.
A 2’s complement of a binary number is achieved by first taking the 1’s complement of a number followed by its 2’s complement.
The 1’s complement of a binary number is obtained by simply inverting each bit.
The 2’s complement of a binary number is obtained by adding a 1 to the 1’s complement of the original number.
In a 2’s complement form all negative binary numbers are represented in their 2’s complement form
All such negative numbers have their most significant bit set to 1 signifying a negative number.
All positive numbers are represented in their original form.
Their most significant bit is a 0 specifying a positive number.

## Slide 5: Range of Numbers
Unsigned
  Positive Numbers Only (0 to 7)
  3-bit
Signed Magnitude
  Positive & Negative Numbers (-7 to 7)
  4-bit
2’s Complement
  Positive & Negative Numbers (-8 to 7)
  4-bit
Notes: What happens if you perform addition of 2 and 7 using unsigned representation?
The answer is 9 and it can not be represented using 3-bit unsigned binary numbers.
An Overflow has occurred.

## Slide 6: Range & Overflow
2 + 7 using 3-bit unsigned binary?
9 overflow?
2 – 7?
Can not represent -7 in unsigned binary

## Slide 7: Range and Overflow
If an addition operation produces a result that exceeds the range of the number system, overflow is said to occur.
If the sum of two positive numbers yields a negative result, the sum has overflowed.
If the sum of two negative numbers yields a positive result, the sum has overflowed.
Otherwise, the sum has not overflowed.
Carryout without overflow. Sum is correct

## Slide 8: Addition and Subtraction with 2’s Complement
0101 +5 0101 +5
0010 +2 1110 -2
0111 +7 10011 +3
1011 -5 1011 -5
1110 -2 0010 +2
11001 -7 1101 -3
Notes: There are four cases of addition
Both numbers are positive
0101 +5
0010 +2
0111 +7
Both numbers are negative
1011 -5
1110 -2
1001 -7 the carry generated from the msb is discarded
One number is positive and its magnitude is larger than the negative number
0101 +5
1110 -2
0011 +3 the carry generated from the msb is discarded
One number is positive and its magnitude is smaller than the negative number
1011 -5
0010 +2
1101 -3
By using signed number based on 2’s complement the addition operation serves to add and subtract numbers.

## Slide 9: Addition and Subtraction 2’s complement vs. Signed
2’s Complement Signed Binary
0101 +5 0101 +5
0010 +2 0010 +2
0111 +7 0111 +7
1011 -5 1101 -5
1110 -2 1010 -2
11001 -7 10111 -7
Notes: Refer to the table of Signed Magnitude and 2’s complement representation of decimal values -8 to 7 discussed in the last lecture.
Compare the addition operation using 2’s complement and signed number representation.
The results for addition using 2’s complement are compatible with the decimal numbers represented in their 2’s complement form.
For example, adding +5 and +2 results in +7 all numbers are represented in their 2’s complement form.
Adding -5 and -2 results in -7, all numbers are represented in their 2’s complement form
Now compare the addition of same numbers represented in their Signed Magnitude form. The addition of +5 and +2 results in +7 all numbers are represented in their signed form.
However, adding -5 and -2 results in -7. -7 is however not represented in its signed form. In fact it represents +7.

## Slide 10: Addition and Subtraction 2’complement vs. Signed
0101 +5 0101 +5
1110 -2 1010 -2
10011 +3 1111 +3
1011 -5 1101 -5
0010 +2 0010 +2
1101 -3 1111 -3
Notes: Consider the addition of +5 and -2 or subtraction of 2 from 5. The answer is +3.
In the 2’s complement form the result 0011 (neglecting the carry bit) is compatible with 2’s complement representation of +3.
In the signed magnitude form the result 1111 doesn’t represent +3 but -7.
In the next example, adding -5 and +2 or subtracting -5 from 2 results in -3.
In the 2’s complement form the result 1101 is compatible with 2’scomplement representation of -3.
In the signed magnitude form the result 1111 doesn’t represent -3 but -7.
Thus representing signed numbers in 2’s complement form allows number to be directly added to perform addition and subtraction. The result would always be correct and in its 2’s complement form.
Thus an adder circuit is able to perform both additions and subtraction if the numbers are represented in their 2’s complement form. No subtractor circuit is required. With signed magnitude form separate adder and subtractor circuits are required or the results have to be converted into signed magnitude form.
Range of 2’s complemented numbers is more than signed magnitude representation.

## Slide 11: Range and Overflow
1011 -5
1101 -3
11000 -8
1011 -5 0101 +5
1100 -4 0100 +4
10111 -9 1001 +9
Notes: Given the choice to represent positive and negative numbers in binary
Unsigned representation is not suitable as it allows only positive numbers
Signed Magnitude allows positive and Negative numbers however addition and subtraction operations results in numbers that are not in signed magnitude form.
2’s complement allows positive and negative numbers, addition and subtraction of numbers in their 2’s complement form results in numbers that are in their 2’s complement form.
The range of 2’s complement numbers is more than signed magnitude representation.

## Slide 12: Range of Binary Numbers
Processors can handle 64-bit unsigned binary values.
Maximum unsigned decimal number is 18.446 x 1018
How to represent larger numbers?
How to represent very small numbers?
How to represent numbers with integer part and fraction part?

## Slide 13: Hexadecimal Number System
Base 16
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
Representing Binary in compact form
  11011000001102 = 1B06 H

## Slide 14: Counting in Hexadecimal
Decimal | Binary | Hexadecimal | Decimal | Binary | Hexadecimal
0 | 0000 | 0 | 8 | 1000 | 8
1 | 0001 | 1 | 9 | 1001 | 9
2 | 0010 | 2 | 10 | 1010 | A
3 | 0011 | 3 | 11 | 1011 | B
4 | 0100 | 4 | 12 | 1100 | C
5 | 0101 | 5 | 13 | 1101 | D
6 | 0110 | 6 | 14 | 1110 | E
7 | 0111 | 7 | 15 | 1111 | F

## Slide 15: Counting in Hexadecimal
Decimal | Hexa- Decimal | Decimal | Hexa- Decimal | Decimal | Hexa- Decimal
16 | 10 | 24 | 18 | 32 | 20
17 | 11 | 25 | 19 | 33 | 21
18 | 12 | 26 | 1A | 34 | 22
19 | 13 | 27 | 1B | 35 | 23
20 | 14 | 28 | 1C | 36 | 24
21 | 15 | 29 | 1D | 37 | 25
22 | 16 | 30 | 1E | 38 | 26
23 | 17 | 31 | 1F | 39 | 27

## Slide 16: Binary-Hexadecimal Conversion
Binary to Hexadecimal Conversion
  11010110101110010110
  1101 0110 1011 1001 0110
  D 6 B 9 6
Hexadecimal to Binary Conversion
  FD13
  1111 1101 0001 0011

## Slide 17: Decimal-Hexadecimal Conversion
Decimal to Hexadecimal Conversion
Indirect Method
  Decimal →Binary → Hexadecimal
Repeated Division by 16

## Slide 18: Decimal-Hexadecimal Conversion
Hexadecimal to Decimal Conversion
Indirect Method
  Hexadecimal →Binary → Decimal
Sum-of-Weights

## Slide 19: Hexadecimal Addition & Subtraction
Hexadecimal Addition
  Carry generated
Hexadecimal Subtraction
  Borrow weight 16

## Slide 20: Repeated Division by 16
Number | Quotient | Remainder
2096 | 131 | 0
131 | 8 | 3
8 | 0 | 8

## Slide 21: Sum-of-Weights
CA02
(C x 163) + (A x 162) + (0 x 161) + (2 x 160)
(12 x 163) + (10 x 162) + (0 x 161) + (2 x 160)
(12 x 4096) + (10 x 256) + (0 x 16) + (2 x 1)
49152 + 2560 + 0 + 2
51714

## Slide 22: Hexadecimal Addition
Carry 1
2AC6 6+5=11d Bh
+ 92B5 C+B=23d 17h
BD7B A+2+1=13d Dh
2+9=11d Bh

## Slide 23: Hexadecimal Subtraction
Borrow 111
92B5 21-6=15d = Fh
- 2AC6 26-C=14d = Eh
67EF 17-A=7d = 7h
8-2=6d = 6h

## Slide 24: Octal Number System
Base 8
0, 1, 2, 3, 4, 5, 6, 7
Representing Binary in compact form
  11011000001102 = 154068

## Slide 25: Counting in Octal
Decimal | Binary | Octal
0 | 000 | 0
1 | 001 | 1
2 | 010 | 2
3 | 011 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7

## Slide 26: Counting in Octal
Decimal | Octal | Decimal | Octal | Decimal | Octal
8 | 10 | 16 | 20 | 24 | 30
9 | 11 | 17 | 21 | 25 | 31
10 | 12 | 18 | 22 | 26 | 32
11 | 13 | 19 | 23 | 27 | 33
12 | 14 | 20 | 24 | 28 | 34
13 | 15 | 21 | 25 | 29 | 35
14 | 16 | 22 | 26 | 30 | 36
15 | 17 | 23 | 27 | 31 | 37

## Slide 27: Binary-Octal Conversion
Binary to Octal Conversion
  11010110101110010110
  011 010 110 101 110 010 110
  3 2 6 5 6 2 6
Octal to Binary Conversion
  1726
  001 111 010 110

## Slide 28: Decimal-Octal Conversion
Decimal to Octal Conversion
Indirect Method
  Decimal →Binary → Octal
Repeated Division by 8

## Slide 29: Decimal-Octal Conversion
Octal to Decimal Conversion
Indirect Method
  Octal →Binary → Decimal
Sum-of-Weights

## Slide 30: Octal Addition & Subtraction
Octal Addition
  Carry generated
Octal Subtraction
  Borrow weight 8

## Slide 31: Repeated Division by 8
Number | Quotient | Remainder
2075 | 259 | 3 (O0)
259 | 32 | 3 (O1)
8 | 4 | 0 (O2)
4 | 0 | 4 (O3)

## Slide 32: Sum-of-Weights
4033
(4 x 83) + (0 x 82) + (3 x 81) + (3 x 80)
(4 x 512) + (0 x 64) + (3 x 8) + (3 x 1)
2048 + 0 + 24 + 3
2075

## Slide 33: Octal Addition
Carry 1
7602 2+1=3d= 3O
+ 5771 0+7=7d= 7O
15573 6+7=13d= 15O
1+7+5=13d =15O

## Slide 34: Octal Subtraction
Borrow 11
7602 2-1=1d 1O
- 5771 8-7=1d 1O
1611 13-7=6d 6O
6-5=1d 1O

## Slide 35: Alternate Representations
BCD Code
Gray Code

## Slide 36: Alternate Representations
BCD (Binary Coded Decimal) Code
Decimal | BCD | Decimal | BCD
0 | 0000 | 5 | 0101
1 | 0001 | 6 | 0110
2 | 0010 | 7 | 0111
3 | 0011 | 8 | 1000
4 | 0100 | 9 | 1001
Notes: Most digital systems display a count value or the time in decimal on 7-segment LED display panels.
Older model Calculator had LED displays instead of the LCD displays.
Since the numbers displayed are in decimal, therefore the binary code used to display the decimal numbers is designed to represent a single digit.
Consider a 2-digit 7-segment display that can display a count value from 0 to 99. To display the two decimal digits two separate binary codes are applied at the 7-segment display circuit inputs. Since each binary code has to specify a digit between 0 and 9 therefore only 10 different binary codes are required.
How many binary bits are required to represent 10 unique codes?
A 4-bit binary code allows 16 different binary combinations to be represented. Only the first 10, 4-bit binary codes are used, the remaining 6 codes are not used.
Thus displaying a 2-digit decimal number 79 would require the digital system to generate two BCD numbers 0111 and 1001 respectively

## Slide 37: Gray Code
Binary Code more than 1 bit change
Electromechanical applications of digital systems restrict bit change to 1
  Shaft encoders
  Braking Systems
Un-Weighted Code

## Slide 38: Gray Code
Decimal | Gray | Binary
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0011 | 0010
3 | 0010 | 0011
4 | 0110 | 0100
5 | 0111 | 0101
6 | 0101 | 0110
7 | 0100 | 0111

## Slide 39: Gray Code Application
Notes: The Diagram shows a disk connected to the shaft of a rotating machine.
The shaded areas on the disk indicate conducting area at a voltage of +5 volts.
The non-shaded area indicate a non-conducting area.
Three stationary brushes A, B and C touch the surface of the rotating disk.
The three brushes are connected to three LED lamps through wires.
As the disk rotates the brushes come in contact with the conducting area and the insulated area. The three LEDs display the position of the rotating shaft in terms of 3-bit numbers.
Thus if the disk on the left rotates in the anti-clockwise direction by 450 the Brush A comes in contact with the conducting strip at 5 volts, which turns on the LED indicating Binary 001.
If the disk continuous its rotation, after a rotation of another 450 ,brush B comes in contact with the conducting strip and brush A comes in contact with the non-conducting strip. Thus LED connected to brush B lights up indicating binary 010.
Thus at any instant of time, the LEDs indicate the angular position of the rotating shaft.
Assume that the three brushes A, B and C are not aligned properly and Brush B is slightly ahead of brushes A and C.
Now if the disk rotates 900 from its start position. Brush A would be in contact with the conducting strip, Brush B due to its misalignment would also be in contact with the conducting strip and brush C would be in contact with the insulated strip.
Thus when the disk rotates the LEDs will show a 001,followed by a 011 for a short duration when the disk rotates from 900 to 910 and then to 010.
Thus due to misalignment the count value jumped from 1 to 3 and then back to 2.
Consider the disk shown on the right. The conducting and non-conducting strips follow a Gray Code pattern 000, 001, 011, 010, 110, 111, 101 and 100 representing decimal 0, 1, 2, 3, 4, 5, 6 and 7.
Now even if the brushes are misaligned, the LEDs would always display the correct count value.

## Slide 40: Alphanumeric Code
Numbers, Characters, Symbols
ASCII 7-bit Code
American Standard Code for Information Interchange
10 Numbers (0-9)
26 Lower Case Characters (a-z)
26 Upper Case Characters (A-Z)
Punctuation and Symbols
32 Control Characters

## Slide 41: ASCII Code
Numbers 0 to 9
ASCII 0110000 (30h) to 0111001 (39h)
Alphabets a to z
ASCII 1100001 (61h) to 1111010 (7Ah)
Alphabets A to Z
ASCII 1000001 (41h) to 1011010 (5Ah)
Control Characters
ASCII 0000000 (0h) to 0011111 (1Fh)

## Slide 42: Alphanumeric Code
Extended ASCII 8-bit Code
Additional 128 Graphic characters
Unicode 16-bit Code

## Slide 43: Error Detection
Digital Systems are very Reliable
Errors during storage or transmission
Parity Bit
  Even Parity
  Odd Parity

## Slide 44: Odd Parity Error Detection
Original data 10011010
With Odd Parity 110011010
1-bit error 110111010
Number of 1s even indicates 1-bit error
2-bit error 110110010
Number of 1s odd no error indicated
3-bit error 100110010
Number of 1s even indicates error

## Slide 45: Summary
2’s Complement
Range and Overflow

## Slide 46: Summary
Hexadecimal Number System
  Binary-Hexadecimal Conversion
  Decimal-Hexadecimal Conversion
Octal Number System
  Binary-Octal Conversion
  Decimal-Octal Conversion

## Slide 47: Summary
Alternate Representations
  BCD Code
  Gray Code
Alphanumeric Codes
  ASCII
Error Detection
  Parity Bit