## Slide 1
Digital Logic & Design
Lecture 06
Copyrights: Dr Waseem Ikram
Engr. Amir Zahoor

## Slide 2: Recap
Implementation Technologies
CMOS
TTL
ECL
PMOS & NMOS
E2CMOS
Notes: CMOS: The most extensively used technology, characterized by low power consumption, switching speed which is slower but comparable to TTL. Has higher chip density than TTL. Due to high input impedance is easily damaged due to accumulated static charge
TTL: Extensively used technology, characterized by fast switching speed and high power consumption
ECL: Used in specialized applications where switching speed is of prime importance, high speed transmission, memories and arithmetic units
PMOS and NMOS: technologies are used in LSI requiring high chip density. Large memories and microprocessors are implemented using these technologies. These ICs have very low power consumption.
E2CMOS: a combination of CMOS and NMOS technologies used to implement Programmable Logic Devices.

## Slide 3: Operational Characteristics
DC Supply Voltage
Noise Margin
Power Dissipation
Frequency Response
Fan Out

## Slide 4: Noise Margin
i/p & o/p signals have a range of voltages
Voltage ranges exceeded due to external noise
Effect on performance under noisy conditions
Margin of error

## Slide 5: TTL Logic Levels
Notes: At the input of any TTL logic gate a logic high signal ‘1’ or a logic low signal ‘0’ is applied.
The VIH is the input voltage range of Logic high signal with a range of 2 to 5 volts
VIH(min) is the minimum acceptable input range for a logic high signal
The VIL is the input voltage range of Logic low signal with a range of 0 to 0.8 volts
VIL(max) is the maximum acceptable input range for a logic low signal
Similarly the output of any TTL logic gate can be at logic high ‘1’ or logic low ‘0’
The VOH is the output voltage range of Logic high signal with a range of 2.4 to 5 volts
VOH(min) is the minimum acceptable output range for a logic high signal
The VOL is the output voltage range of Logic low signal with a range of 0 to 0.4 volts
VOL(max) is the maximum acceptable output range for a logic low signal
Consider that the output of an And gate is connected to the input of an OR gate
What are the voltage ranges for the two gates?

## Slide 6: CMOS Logic Levels
Notes: At the input of any CMOS 5 volt series logic gate a logic high signal ‘1’ or a logic low signal ‘0’ is applied.
The VIH is the input voltage range of Logic high signal with a range of 3.5 to 5 volts
VIH(min) is the minimum acceptable input range for a logic high signal which is 3.5 volts
The VIL is the input voltage range of Logic low signal with a range of 0 to 1.5 volts
VIL(max) is the maximum acceptable input range for a logic low signal which is 1.5 volts
Similarly the output of any CMOS 5 volt series logic gate can be at logic high ‘1’ or logic low ‘0’
The VOH is the output voltage range of Logic high signal with a range of 4.4 to 5 volts
VOH(min) is the minimum acceptable output range for a logic high signal which is 4.4 volts
The VOL is the output voltage range of Logic low signal with a range of 0 to 0.33 volts
VOL(max) is the maximum acceptable output range for a logic low signal which is 0.33 volts
At the input of any CMOS 3.3 volt series logic gate a logic high signal ‘1’ or a logic low signal ‘0’ is applied.
The VIH is the input voltage range of Logic high signal with a range of 2 to 3.3 volts
VIH(min) is the minimum acceptable input range for a logic high signal which is 2 volts
The VIL is the input voltage range of Logic low signal with a range of 0 to 0.8 volts
VIL(max) is the maximum acceptable input range for a logic low signal which is 0.8 volts
Similarly the output of any CMOS 3.3 volt series logic gate can be at logic high ‘1’ or logic low ‘0’
The VOH is the output voltage range of Logic high signal with a range of 2.4 to 3.3 volts
VOH(min) is the minimum acceptable output range for a logic high signal which is 2,4 volts
The VOL is the output voltage range of Logic low signal with a range of 0 to 0.4 volts
VOL(max) is the maximum acceptable output range for a logic low signal which is o.4 volts
The two CMOS 5 volts and the 3.3 volts series can not be mixed.

## Slide 7: Unpredictable Behaviour due to Noise
Notes: Consider the CMOS 5 volt series AND gate
Input A of the AND gate is permanently connected to logic high of +5 volts.
Input B of the AND gate is connected to the output of some other gate.
The signal at input B of the AND gate can vary between logic 0 and logic 1.
Consider that the input B is at logic high state with VIH = 4.2 volts which is within the valid voltage range of VIH between 5 and 3.5 volts
Consider a voltage generated due to some external noise added to the 4.2 volt signal.
A sharp dip in the input voltage due to the noise brings the input voltage down to 3 volts for a very short duration.
The 3 volt input is below the minimum input voltage limit of 3.5 volts for logic high input voltage.
This dip in the voltage even for a short duration will result in an output of logic low for a short interval of time, which will cause the logic circuit to malfunction.

## Slide 8: Logic Levels and Noise Margin
VNH = VOH(min) – VIH(min)
VNL = VIL(max) – VOL(max)
Notes: CMOS 5 volt series AND gates connected together.
The first AConsider two ND gate has both its inputs connected to logic high, therefore the output of the gate is guaranteed to be logic high.
The logic high voltage output of the first AND gate is assumed to be at 4.6 volts well within the valid VOH range of 5-4.4 volts.
Assume the same noise signal (as described earlier) being added to the output signal of the first AND gate.
The sharp dip due to noise brings the VOH voltage down to 3.4 volts with reference to the VOH of 4.6 volts.
3.4 volts is lower than the VIH(min) of by the input 3.5 volts required of the second AND gate. Thus the circuit will malfunction.
Since VOH(min) is guaranteed to be at 4.4 volts therefore a noise signal being added to 4.4 volts can bring VOH voltage down to a minimum of 3.5 volts which is the acceptable minimum range for VIH
Anything below 3.5 will cause the second gate to malfunction.

## Slide 9: Logic Levels and Noise Margin
CMOS Noise Margins
  VNH = VOH(min) – VIH(min) = 4.4 - 3.5 = 0.9 v
  VNL = VIL(max) – VOL(max) = 1.5 – 0.33 = 1.17 v
  VNH = VOH(min) – VIH(min) = 2.4 – 2.0 = 0.4 v
  VNL = VIL(max) – VOL(max) = 0.8 – 0.4 = 0.4 v
TTL Noise Margins
  VNH = VOH(min) – VIH(min) = 2.4 - 2.0 = 0.4 v
  VNL = VIL(max) – VOL(max) = 0.8 – 0.4 = 0.4 v

## Slide 10: Power Dissipation
Power Dissipation constant for TTL
Power Dissipation varies with frequency for CMOS

## Slide 11: TTL Power Dissipation
Gate Output High (ICCH)
Gate Output Low (ICCL)
Average Power Dissipated
Pcc = Vcc Icc
Pcc = Vcc (ICCH + ICCL)/2

## Slide 12: TTL Power Dissipation

## Slide 13: CMOS Power Dissipation
Power Dissipation varies with frequency for CMOS
PD = (CPD+ CL).VDD2.f
CPD is the internal power dissipation capacitance
CL is the external load dissipation capacitance
VDD is the supply voltage
f is the transition frequency of the output signal
Notes: The power dissipation of a HCMOS gate is 2.75 μW under static conditions and 170 μW at 100 KHz.

## Slide 14: Propagation Delay and Frequency Response
Propagation Delay
Limits frequencies at which gate can operate
Notes: The Propagation Delay of a gate limits the frequencies at which the gate can work. Larger the Propagation Delay lower is the frequency at which the gate can operate. Smaller the Propagation Delay higher the frequency at which the gate can operate.
A Gate with a delay of 3 nsec is faster than a gate with a 10 nsec delay.

## Slide 15: Propagation Delay
tPHL tPLH
Notes: Propagation Delays for logic gates are specified by tPHL and tPLH parameters
The NOT gate is shown
The output of the NOT gate changes from high to low after a delay of time specified by tPHL after the input changes from low to high.
The output of the NOT gate changes from low to high after a delay of time specified by tPLH after the input changes from high to low
The delay time is measured at the 50% transition mark.

## Slide 16: Propagation Delay
Notes: The AND gate is shown. The input B of the AND gate is permanently connected to H, where as input A varies between H and L.
The output of the AND gate changes from low to high after a delay of time specified by tPLH after the input changes from low to high.
The output of the AND gate changes from high to low after a delay of time specified by tPHL after the input changes from high to low
The delay time is measured at the 50% transition mark.

## Slide 17: Speed-Power Product (SPP)
SPP = tP PD
Expressed in Joules (J) units of energy
Lower the SP product better is the performance

## Slide 18: Fan-Out
Number of same series gates that a gate can drive.
Fan-Out for TTL circuits is fixed
Fan-Out for CMOS circuits is related to operational frequency.
Fan-Out decreases with increased frequency

## Slide 19: Fan-Out for TTL Loads
Unit Loads = IOH/IIH = IOL/IIL
= 400 μA/40 μA = 16 mA/1.6 mA = 10
Notes: The fan-out of a logic gate is the maximum number of inputs of the same series in an IC family that can be connected to a gate’s output and still maintain the output voltage levels within the specified limits.
The output current at logic high is IOH = 400 μA
The input current at logic high is IIH = 40 μA
Thus a gate at logic high can source current to another gate connected to its output.
Similarly
The output current at logic low is IOL = 16 mA
The input current at logic low is IIL = 1.6 mA
Thus a gate output at logic low can sink current from another gate connected to its output.
To calculate the unit load that can be connected the Unit load formula is used
Unit Loads = IOH/IIH = IOL/IIL = 400 μA/40 μA = 16 mA/1.6 mA = 10

## Slide 20: Fan-Out for TTL Loads
Notes: Considering that
The output current at logic high is IOH = 400 μA
The input current at logic high is IIH = 40 μA
A gate’s output can be connected to inputs of a maximum of 10 gates as 400 μA can be equally distributed amongst 10 gates that is 40 μA each.

## Slide 21: Fan-Out for TTL Loads
Notes: Similarly considering that
The output current at logic low is IOL = 16 mA
The input current at logic low is IIL = 1.6 mA
A gate’s output can be connected to inputs of a maximum of 10 gates as 1.6 mA from each of the 10 gates can be sunk by it, that is 16 mA
Unit Loads = IOH/IIH = IOL/IIL = 400 μA/40 μA = 16 mA/1.6 mA = 10

## Slide 22: Fan-Out for CMOS Loads
Notes: CMOS loading is different from TTL loading as the type of transistors used in CMOS circuits presents a capacitive load to the driving gate.
When the output of the driving gate is high the input capacitance of the load gate is charging and when the output of the driver gate is low the load gate is discharging.
When more load gates are added the input capacitance increases as input capacitances are being connected in parallel. With the increase in the capacitance, charging and discharging time increases, reducing the maximum frequency at which the gate can operate.
Therefore the fan-out of a CMOS gate depends upon the maximum frequency of operation. Fewer the load gates greater the maximum frequency of operation.

## Slide 23: TTL Series
 | 74 | 74S | 74LS | 74AS | 74ALS | 74F
Performance Rating |  |  |  |  |  | 
Propagation Delay (ns) | 9 | 3 | 9.5 | 1.7 | 4 | 3
Power Dissipation (mW) | 10 | 20 | 2 | 8 | 1.2 | 6
Speed-Power product (pJ) | 90 | 60 | 19 | 13.6 | 4.8 | 18
Max. Clock Rate (MHz) | 35 | 125 | 45 | 200 | 70 | 100
Fan-out (same series) | 10 | 20 | 20 | 40 | 20 | 33

## Slide 24: CMOS Series
 | 74HC | 74AC | 74AHC
Propagation Delay (ns) | 18 | 5 | 3.7
Power Dissipation (mW) Static | 0.00275 | 0.0055 | 0.00275
Power Dissipation (mW) at 100KHz | 0.0625 | 0.08 | 0.0625
Speed-Power product (pJ) at 100KHz | 1.125 | 0.4 | 0.23
Max. Clock Rate (MHz) | 50 | 160 | 170
 | 74LV | 74LVC | 74ALVC
Propagation Delay (ns) | 9 | 4.3 | 3
Power Dissipation (mW) Static | 0.0016 | 0.0008 | 0.0008
Max. Clock Rate (MHz) | 90 | 100 | 150

## Slide 25: Boolean Algebra
Variable
Complement
Literal
Notes: Variable: A variable is a symbol usually an uppercase letter used to represent a logical quantity.
A variable can have a 0 or 1 value.
Complement: A complement is the inverse of a variable and is indicated by a bar over the variable.
Complement of variable X is X*
If X = 0 then X*= 1 and if X = 1 then X*= 0
Literal: A Literal is a variable or the complement of a variable. X and X* are literals

## Slide 26: Boolean Addition & Multiplication
Boolean Addition performed by OR gate
Sum Term describes Boolean Addition
Boolean Multiplication performed by AND gate
Product Term describes Boolean Multiplication

## Slide 27: Boolean Addition
Sum of literals
Sum term = 1 if any literal = 1
Sum term = 0 if all literals = 0
Notes: Sum term is described as sum of literals

## Slide 28: Boolean Multiplication
Product of literals
Product term = 1 if all literals = 1
Product term = 0 if any one literal = 0
Notes: Product term is described as product of literals

## Slide 29: Laws, Rules & Theorems of Boolean Algebra
Commutative Law
  for addition and multiplication
Associative Law
  for addition and multiplication
Distributive Law
Rules of Boolean Algebra
Demorgan’s Theorems

## Slide 30: Commutative Law
Commutative Law for Addition
A + B = B + A
Commutative Law for Multiplication
A.B = B.A
Notes: The basic laws of Boolean Algebra are the same as ordinary algebra and hold true for any number of variables

## Slide 31: Associative Law
Associative Law for Addition
A + (B + C) = (A + B) + C
Notes: The sum term B OR C Ored with A is the same as sum term A OR B Ored with C

## Slide 32: Associative Law
Associative Law for Multiplication
A.(B.C) = (A.B).C
Notes: The product term BC Anded with A is the same as AB Anded with C

## Slide 33: Distributive Law
A.(B + C) = A.B + A.C

## Slide 34: Rules of Boolean Algebra
A + 0 = A
A + 1 = 1
A.0 = 0
A.1 = A
A + A = A
A + = 1
A.A = A
A. = 0
= A
A + A.B = A
A + = A + B
(A+B).(A+C)
= A+B.C
Notes: A+A*B = A(B+1)+A*B using rule 2
=AB+A+A*B
=A+AB+A*B
= A+B
(A+B)(A+C) = A+AC+AB+BC
=A+BC

## Slide 35: Demorgan’s Theorems
First Theorem
Second Theorem
Notes: Demorgan’s First Theorem states: The complement of a product of variables is equal to the sum of the complements of the variables.
Demorgan;s Second Theorem states: The complement of sum of variables is equal to the product of the complements of the variables

## Slide 36: Demorgan’s Theorems
Any number of variables
Combination of variables
Notes: Demorgan’s Theorems can be applied to expressions having any number of variables
Demorgan’s Theorem can be applied to a combination of other variables

## Slide 37: Boolean Analysis of Logic Circuits
Boolean Algebra provides concise way to represent operation of a logic circuit
Complete function of a logic circuit can be determined by evaluating the Boolean expression using different input combinations
Notes: Boolean algebra provides a concise way to represent the operation of a logic circuit.
The complete function of the logic circuit can be determined by evaluating the Boolean expression using different input combinations.

## Slide 38: Boolean Analysis of Logic Circuits
From the expression, the output is a 1 if variable D = 1 and =1
=1 if AB=1 or C=0

## Slide 39: Boolean Analysis of Logic Circuits
Inputs |  |  |  | Output | Inputs |  |  |  | Output
A | B | C | D | F | A | B | C | D | F
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1

## Slide 40: Simplification using Boolean Algebra
Notes: Many times a Boolean expression has to be simplified using laws, rules and theorems of Boolean Algebra.
The simplified expression results in fewer variables and a simpler circuit.

## Slide 41: Simplification using Boolean Algebra
AB + A(B+C) + B(B+C)
= AB + AB + AC + BB +BC
= AB + AC + B + BC
= AB + AC + B
= B + AC

## Slide 42: Simplified Circuit

## Slide 43: Standard forms of Boolean Expressions
Sum-of-Products form
Product-of-Sums form
Notes: Sum-of-Product (SOP) form: When two or more product terms are summed by Boolean addition, the result is a Sum-of-Product or SOP expression
Product-of-Sum (POS) form: When two or more sum terms are multiplied by Boolean multiplication, the result is a Product-of-Sum or POS expression
The Domain of an SOP and POS expression is the set of variables contained in the expression, both complemented and un-complemented.
A SOP and POS expression can have a single variable term such as A
A SOP and POS expression can not have a term of more than one variable having an over bar extending over the entire term.

## Slide 44: Standard forms of Boolean Expressions
Sum-of-Products form
AB + ABC
ABC + CDE +
Product-of-Sums form

## Slide 45: Implementation of SOP expression

## Slide 46: Implementation of POS expression

## Slide 47: Conversion of general expression to SOP form
Notes: Any logical expression can be converted into SOP form by applying techniques of Boolean Algebra