## Slide 1
Digital Logic & Design
Lecture 10

## Slide 2: Combinational Logic
Implementation of SOP using AND-OR
Implementation of POS using OR-AND

## Slide 3: SOP Implementation
Notes: The diagram shows the general architecture of the SOP Implementation.
SOP expression is implemented by the AND-OR combination of gates.
The AND gates produce the product terms.
Outputs of all the AND gates are connected to a single multiple input OR gate for sum of products.
The product terms comprise of literals in their complemented form and un-complemented form which are implemented by NOT gates connected to the inputs of the AND gates.

## Slide 4: POS Implementation
Notes: The diagram shows the general architecture of the POS Implementation.
POS expression is implemented by the OR-AND combination of gates.
The OR gates produce the sum terms.
Outputs of all the OR gates are connected to a single multiple input AND gate for product of sum terms
The sum terms comprise of literals in their complemented form and un-complemented form which are implemented by NOT gates connected to the inputs of the OR gates.

## Slide 5: Design and Implementation of Digital Circuits
Function Table
Simplification of Expression
Implementation

## Slide 6: Adjacent 1s Detector Circuit
SOP Implementation
  Directly from function table
Simplified implementation
Implementation using NAND gates

## Slide 7: Adjacent 1s Detector Function
Input |  |  |  | Output | Input |  |  |  | Output
A | B | C | D | F | A | B | C | D | F
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Notes: The Adjacent 1s detector circuit accepts a 4-bit binary input and generates a 1 output when it detects a combination of two adjacent 1s.
The function diagram shows the 16 possible input combinations and the corresponding outputs.
Thus for the input combinations 0011, 0110, 0111, 1011, 1100, 1101, 1110 and 1111 the output function is a 1.
The information provided by the function table can be directly implemented to form the Adjacent 1s Detector circuit
How many AND gates are required?
Eight gates to implement the 8 minterms.
How many OR gates are required?
A single eight input OR gate is required to sum all the eight product terms.
Some NOT gates are also required to implement complemented literals in some of the product terms.

## Slide 8: SOP Implementation
Notes: The SOP based implementation of the Adjacent 1s detector circuit is shown implemented directly from the function table.
This implementation uses maximum number of gates.
The total gate count is
one 8 input OR gate
eight 4 input AND gates
ten NOT gates
All together 19 gates are required.
The increased number of gates increases the cost, the size of the circuit, the power requirement and the propagation delay which is of the order of three gates.

## Slide 9: SOP Expression Simplification
AB\CD | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 0
01 | 0 | 0 | 1 | 1
11 | 1 | 1 | 1 | 1
10 | 0 | 0 | 1 | 0
Notes: An appropriate way to implement the Adjacent 1s detector circuit is to simplify the SOP boolean expression represented by the function table and then implement the circuit based on the simplified expression.
The function table information is directly mapped to a 4-variable K-map
The 1s are grouped together forming three product terms
AB, CD and BC

## Slide 10: SOP based Simplified Circuit
Notes: The simplified circuit is implemented using
three 2-input AND gates
And a single 3-input OR gate.
The total circuit count is 4 gates.
The cost of the circuit reduces
The size of the circuit reduces
The power requirement of the circuit reduces
And the propagation delay has reduced from three gate delay to two gate delay.

## Slide 11: NAND based Implementation
Notes: The simplified 4 gate circuit can be implemented using only NAND gates without a change in the total number of gates.
Bubbles representing NOT gates are placed at the output of the three AND gates. Converting the three AND gates to NAND gates.
To balance out the three NOT gates added at the outputs of the three AND gates. Three bubbles representing three NOT gates are also placed at the three inputs of the OR gate.
The Resulting OR gate symbol with three bubbles at the three inputs is an alternate symbol for a three input NAND gate.
The NAND based circuit is shown.

## Slide 12: Adjacent 1s Detector Circuit
POS Implementation
  Directly from function table
Simplified Implementation
Implementation using NOR Gates

## Slide 13: POS Implementation
Notes: The POS based implementation of the Adjacent 1s detector circuit is shown implemented directly from the function table.
This implementation uses maximum number of gates.
The total gate count is
one 8 input AND gate
eight 4 input OR gates
ten NOT gates
All together 19 gates are required.
The increased number of gates increases the cost, the size of the circuit, the power requirement and the propagation delay which is of the order of three gates.

## Slide 14: POS Expression Simplification
AB\CD | 00 | 01 | 11 | 10
00 | 0 | 0 | 1 | 0
01 | 0 | 0 | 1 | 1
11 | 1 | 1 | 1 | 1
10 | 0 | 0 | 1 | 0
Notes: An appropriate way to implement the Adjacent 1s detector circuit is to simplify the POS boolean expression represented by the function table and then implement the circuit based on the simplified expression.
The function table information is directly mapped to a 4-variable K-map
The 0s are grouped together forming three sum terms
A+C, B+C and B+D

## Slide 15: POS based Simplified Circuit
Notes: The simplified circuit is implemented using
three 2-input OR gates
And a single 3-input AND gate.
The total circuit count is 4 gates.
The cost of the circuit reduces
The size of the circuit reduces
The power requirement of the circuit reduces
And the propagation delay has reduced from three gate delay to two gate delay.

## Slide 16: NOR based Implementation
Notes: The simplified 4 gate circuit can be implemented using only NOR gates without a change in the total number of gates.
Bubbles representing NOT gates are placed at the output of the three OR gates. Converting the three OR gates to NOR gates.
To balance out the three NOT gates added at the outputs of the three OR gates. Three bubbles representing three NOT gates are also placed at the three inputs of the AND gate.
The Resulting AND gate symbol with three bubbles at the three inputs is an alternate symbol for a three input NOR gate.
The NOR based circuit is shown.

## Slide 17: Operation of Circuit
Represented through a timing diagram
Timing diagram of 8 time intervals
Each interval representing a new input

## Slide 18: POS based Simplified Circuit

## Slide 19: Operation of Circuit
Notes: The timing diagram describes the operation of the circuit for the POS based simplified circuit for intervals t0 to t8
A, B, C and D are the inputs to the circuit.
The timing diagram shows the inputs A, B, C and D changing with time.
The timing signals 1, 2 and 3 represent the outputs of the OR gates 1, 2 and 3.
The timing signal F represents the output of the circuit.
At interval t0 the input ABCD to the circuit is 0000, the outputs of the three OR gates is 00 and 0 and the circuit output is also 0
At tie interval t3 the input ABCD to the circuit is 0011, the outputs of OR gates 1,2 and 3 are 111. The output F is also a 1.
The circuit has detected adjacent 1s.
At interval t6 the input ABCD to the circuit is 0110, the outputs of OR gates 1,2 and 3 are 111. The output F is 1 indicating adjacent 1s.
The operation of the circuit which is based on the POS simplified expression also proves that a POS based expression determined from the truth table and K-map results in a circuit which operates in an identical manner to that of a SOP based circuit.

## Slide 20: Active low/high inputs/outputs
Active output state represented by 1 or 0
Active input state represented by 1 or 0
A bubble at output represents active low output
A bubble at input represents active low input
Notes: BCD to 7-Segmnet display circuit sets segment output to 1
Comparator circuit sets A>B, A=B, A< B output to 1
Odd-Prime Number Detector Circuit
Adjacent 1s detector sets output to 1 when it detects adjacent 1s

## Slide 21: Active low/high inputs/outputs
Notes: AND gate performs AND operation on two active high inputs to result in an active high output
NAND gate performs AND operation on two active high inputs resulting in an active low output
OR gate performs OR operation on two active high inputs to result in an active high output
NOR gate performs OR operation on two active high inputs to result in an active low output

## Slide 22: Active-high inputs & outputs
Notes: The simplified SOP based implementation has an active high output
The circuit can be implemented to have an active low output by connecting a NOT gate at the output of the circuit.
Now when ever adjacent 1s are detected the circuit output is set to 0.
The circuit also is shown to have active-high inputs
The circuit can work with active–low input producing an active high output if NOT gates are connected to the inputs of all the AND gates.

## Slide 23: Active-high inputs & outputs
Notes: Consider now the SOP based circuit which has active high inputs and active high output.
If the inputs of the circuit are made active low and the output of the circuit is also made active low then bubbles are added at all the inputs of the three AND gates.
A bubble is also added to the output of the OR gate.
The bubbles added at the input of the AND gate represent the alternate symbol for the NOR gate.
Similarly the bubble added to the output of the OR gate also makes it a NOR gate.
By modifying the circuit to have active low inputs and outputs.
The circuit sets the output F to active 0 to indicate detection of adjacent 1s.
Since the inputs are also represented by active low therefore the input ABCD 0000 actually represents 1111, similarly ABCD active low input 0001 actually represents 1110.

## Slide 24: Operation of Circuit
Notes: The timing diagram describes the operation of the circuit for the intervals t0 to t8
The timing signals A, B, C and D represent the active-low inputs applied at the inputs.
The timing signals 1, 2 and 3 represent the outputs of the NOR gates 1, 2 and 3 respectively.
The timing signal F represents the active-low output.
At interval t0 the active-low input at inputs ABCD is 0000 which actually represents 1111. The active-low output F is 0 which indicates that adjacent 1s have been detected.
Similarly at intervals t1 to t4, the active-low inputs ABCD 0001, 0010, 0011 and 0100 which actually represent the numbers 1110, 1101, 1100 and 1011, the output is 0 indicating that adjacent 1s have been detected.

## Slide 25: Odd-Parity Generator Circuit
Circuit checks the 4-bit data
Generates a parity bit (odd)
Data + parity bit add up to odd number of 1s

## Slide 26: Odd-Parity Function
Input |  |  |  | Output | Input |  |  |  | Output
D3 | D2 | D1 | D0 | P | D3 | D2 | D1 | D0 | P
0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
Notes: The function table represents the 16 possible combination of 4 data bits
The 4 data bits are represented by variables D3, D2, D1 and D0
The output P represents the state of the Parity bit.
Since Odd parity is being used therefore the 4-bit data and the parity bit should add up to give odd number of 1s.
The function table shows the Parity bit set to 1 when the 16, 4-bit data input combinations have no 1s or an even number of 1s.

## Slide 27: SOP Expression SImplification
D3D2\D1D0 | 00 | 01 | 11 | 10
00 | 1 | 0 | 1 | 0
01 | 0 | 1 | 0 | 1
11 | 1 | 0 | 1 | 0
10 | 0 | 1 | 0 | 1
Notes: The information in the function table is mapped directly to a four variable K-map to simplify the Boolean expression represented by the Odd-parity generator function.
None of the 1s mapped in the K-map are adjacent to each other thus the function mapped to the K-map can not be simplified.
However, using the Rules of Boolean algebra, applying Demorgan’s theorems and knowing the function table of XOR and XNOR gates the Boolean expression can be simplified

## Slide 28: Simplifying Expression
Notes: The expression has 8 minterms
The expression for the sake of simplification is represented in terms of variables A, B, C and D instead of D3, D2, D1 and D0 respectively.
The expression can be rewritten in terms of the common product terms A*B*, A*B, AB and AB* and sum of product terms C*D*+CD and C*D+CD*
The expression can be further represented in terms of sum of product terms C*D*+CD, A*B*+AB, C*D+CD* and A*B+AB*
The four sum of product terms represent C XNOR D, A XNOR B, C XOR D and A XOR B
The expression if seen in terms of X and Y simplifies to A XOR B XNORed with C XOR D

## Slide 29: Odd-Parity Generator Circuit
Notes: Thus the original 8 minterm expression is implemented using 2 XOR and a single XNOR gate

## Slide 30: Operation of Odd-Parity circuit
Notes: The timing diagram shows the operation of the Odd-Parity generator circuit.
The A, B, C and D timing diagrams represent the changing 4-bit data values.
During time interval t0 the 4-bit data value is 0000, during time interval t1, the data value changes to 0001.
Similarly during time intervals t2, t3, t4 up to t8 the data values change to 0010, 0011, 0100 and 1000 respectively.
During interval t0 the output of the two XOR gates is 00, therefore the output of the XNOR gate is 1.
At interval t1, the outputs of the two XOR gates is 10, therefore the output of the XNOR gate is 0.
The output P can similarly be traced for intervals t2 to t8

## Slide 31: XOR & XNOR Gates
XOR function
XNOR function

## Slide 32: XOR Gate
Notes: The XOR operation performs a comparison function.
An XOR operation detects dissimilar inputs.
The XOR gate can be implemented using a combination of NOT-AND-OR gates.
Since the function performed by the XOR gate is commonly used in digital circuits therefore XOR gates are available in Integrated circuit form which can be readily used instead of implementing a XOR circuit based on NOT-AND-OR combination of gates.

## Slide 33: XNOR Gate
Notes: The XNOR operation performs a comparison function.
An XNOR operation detects similar inputs.
The XNOR gate can also be implemented using a combination of NOT-AND-OR gates.
Since the function performed by the XNOR gate is commonly used in digital circuits therefore XNOR gates are available in Integrated circuit form which can be readily used instead of implementing a XNOR circuit based on NOT-AND-OR combination of gates.

## Slide 34: Combinational Functional Devices
Comparators
BCD to 7-Segment
Parity Generator Circuit

## Slide 35: Half & Full Adders
Half Adder
Full Adder

## Slide 36: Half & Full Adders
Notes: The block diagrams represent a Full-Adder and a Half-Adder.
A single bit binary adder circuit basically adds two bits and a carry bit, generated by the addition of the least significant bits. The output of the single bit adder circuit generates a sum bit and a carry bit.
An adder circuit that only has two bit input representing the two single bit numbers A and B and does not have the carry bit input from the least significant digit is regarded as a half-adder.
An adder circuit that has three inputs, two bits representing the two single bit numbers A and B, and the third bit represents the Carry in bit is regarded as a full-adder

## Slide 37: Half-Adder
Function Table
Expression
Logic Circuit

## Slide 38: Half-Adder Function Table
Input |  | Output | 
A | B | Sum | Carry Out
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 39: Half-Adder Circuit

## Slide 40: Full-Adder
Function Table
Expression
Logic Circuit

## Slide 41: Full-Adder Function Table
Input |  |  | Output | 
A | B | Carry In (C) | Sum | Carry Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 42: Sum Expression

## Slide 43: Carry Out Expression

## Slide 44: Full-Adder Circuit

## Slide 45: Full-Adder
Full-Adder = Half-Adder + Half-Adder

## Slide 46: Full-Adder based on Two Half-Adders

## Slide 47: Parallel Binary Adder
Multiple Single bit Full-Adder connected in Parallel

## Slide 48: 4-bit Parallel Adder

## Slide 49: Carry Propagation
Carry Ripple
Look-Ahead Carry Circuits

## Slide 50: Look-Ahead Carry Circuit
Notes: The P output is called the Carry Propagate.
The G output is called the Carry Generate as it generates a carry when A and B are both 1 regardless of C in.

## Slide 51: Sum & Carry Expressions

## Slide 52: Carry Expressions

## Slide 53: Look-Ahead Carry Generator

## Slide 54: MSI-Adders
74LS83A
74LS283
16-pin ICs
4-bit A input
4-bit B input
4-bit Sum output
1-bit Carry in
1-bit Carry Out

## Slide 55: 12-bit Parallel Adder
Notes: The first 4-bit Adder chip on the extreme right is used to add bits 0 to 3, the least significant four bits of the two 12 bit numbers.
The second 4-bit Adder chip in the middle is used to add bits 4 to 7, the next most significant bits of the two 12 bit numbers.
Finally, the third 4-bit Adder chip on the extreme left is used to add the most significant bits 8 to 11 of the 12-bit numbers.
Similarly the 4-bit adder chip on the extreme right generates least significant Sum outputs 0 to 3.
The second 4-bit Adder chip generates Sum output for bits 4 to 7.
The third 4-bit Adder chip on the extreme left generates the Sum outputs for most significant bits 8 to 11.
The Carry out is generated by the left most 4-bit Adder. It is shown as C12
Similarly the Carry in is shown connected to the right most 4-bit adder. It is represented by C0.
Carry out of the first 4-bit Adder on the extreme right is connected to the Carry In of the 4-bit adder in the middle. It is represented as C4.
The Carry out of the middle 4-bit adder is connected to the Carry in of the 4-bit Adder on the extreme left. It is represented by C8.