## Slide 1
DECODER
A decoder is a circuit that converts binary information from
the n coded inputs to a maximum of 2n unique outputs
Multiple Inputs and Multiple Outputs

## Slide 3
Example: 3 to 8 line decoder

## Slide 4
DECODERS

## Slide 5
DECODER
Example: 2 to 4 line decoder

## Slide 6
LARGE DECODERS

## Slide 7: Function Implementation via Decoder
Full Adder
Input |  |  | Output | 
A | B | Carry In (C) | Sum | Carry Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 9
ENCODERS
An encoder has 2n or fewer input lines and n output values
Opposite of the decoder function
The output lines generate the binary code corresponding to
the input value
A2=D4+D5+D6+D7;
A1=D2+D3+D6+D7;
A0=D1+D3+D5+D7
Example:

## Slide 10
ENCODERS
Priority Encoder
The operation of the priority encoder is such that if two or
more inputs are equal to 1 at the same time, the inputs
having the highest priority takes precedence
Example: A four input priority encoder

## Slide 11
ENCODERS
Priority Encoder
The Xs in output columns represent don’t care conditions
The Xs in input columns are used to represent both 1s and 0s
The output V (V for valid) is set to 1 only when one or more
inputs are equal to 1
If all inputs are equal to 0, then V is set to 0

## Slide 13
MULTIPLEXERS
a multiplexer selects one of several input signals
and forwards the selected input into a single line
n inputs, one output and s select inputs (2^s = n)

## Slide 14
MULTIPLEXERS
Selection Inputs: Input variables which control the selection of
input lines. For 2n input lines we need n selection inputs
An 2n input, m output multiplexer is called 2n-to-m line MUX
A 4-to-1 line MUX is shown above

## Slide 15
MULTIPLEXERS
Enable Input
An enable input controls the operation of the unit
It is useful for combining two or more multiplexers into a
single large multiplexer
Multiple Bits Selection
Multiplexer blocks can be combined in parallel to perform
selection on multiple bit quantities
These have common selection and enable lines

## Slide 16
MULTIPLEXERS
Quadruple
2-to-1 line MUX
It has 4 multiplexers
each capable of
selecting one of two
input lines
The circuit may also
be viewed as a
selector of one of two
sets of data lines,
where each set has
4 lines

## Slide 17
MULTIPLEXERS
Selection Inputs: Input variables which control the selection of
input lines. For 2n input lines we need n selection inputs
An 2n input, m output multiplexer is called 2n-to-m line MUX
A 4-to-1 line MUX is shown above

## Slide 18
MULTIPLEXERS
We can implement a Boolean function of n variables with a
multiplexer with n-1 selection inputs
The first n-1 variables of the function are connected to the
selection inputs of the multiplexer and the remaining
nth variable is used for data inputs
Boolean Function Implementation

## Slide 19
MULTIPLEXERS
Boolean Function Implementation
F = Σm(1,2,6,7)

## Slide 20
MULTIPLEXERS
Boolean Function Implementation
F = Σm(1,3,4,11,12,13,14,15)

## Slide 21
MULTIPLEXERS
Boolean Function Implementation
F = Σm(2,3,5,6,8,9,12,14)

## Slide 22
MULTIPLEXERS
Demultiplexers
A demultiplexer receives information from a single line and
transmits it to one of 2n output lines
A 1-to-4 line demultiplexer: